## Slide 1: L 17 - Thermodynamics [2]
Today’s topics
  Practical thermal effects
  Devices for temperature measurement
  Mechanisms of heat transfer
Science dealing with the relationship
between thermal energy (random molecular motion) and work (organized motion), and the conversion of one into the other

## Slide 2: Thermal Energy and Work
The random motion of the atoms is thermal energy
The sum of all the energies of all the atoms is called the internal energy
The upward motion of the piston is work energy
Some of the internal energy is used to do work in lifting the piston

## Slide 3: Thermocouples
180 F
AMPS
two different metals

## Slide 4: Thermocouples- measure Temp.
Is composed of 2 wires of different metals welded together
when the tip gets hot an electrical current is produced
The current is proportional to the temperature
It can be used over a wide range of temperatures
500 °F

## Slide 5: Thermocouples used as safety devices
a thermocouple is used in gas heaters, dryers, and fireplaces to protect against explosions
a thermocouple is placed in the pilot light
as long as the pilot light is on, the thermocouple is hot and current flows
a circuit detects the current and allows the main gas valve to open
if the pilot light is out, the circuit prevents the main gas valve from opening
Pilot light
Thermocouple
current gas

## Slide 6: Thermal Expansion
The length of a bar of metal increases when it is heated
Actually, all dimensions expand by the same percentage
Expansion must be taken into account when designing roads and bridges in climates that vary significantly from winter to summer – all materials expand, steel, concrete, asphalt . . .
Metal bar at T1
Metal bar at T2 > T1
L2
L1

## Slide 7: Thermal Expansion
Most substances expand when heated
We use a parameter, a called the coefficient of thermal expansion to quantify this effect
The length of a metal bar increases from L0 to L (DL = L – L0), when it is heated from T1 to T2 (DT = T2 –T1)
Change in length = DL = a L0 DT
For copper, a = 17×10-6 per deg. C
Change DL = (17×10-6 per C)(1 m)(100 C-22 C) = 0.0013 m = 1.3 mm

## Slide 8: Coefficients of linear expansion
SUBSTANCE | a (per deg C)
aluminum | 23 × 106
brass | 19 × 106
glass | 9 × 106
rubber | 80 × 106
Ice | 51 × 106
lead | 29 × 106
steel | 11 × 106
concrete | 10 × 106

## Slide 9: winter/summer expansion gaps

## Slide 10
expansion gaps on bridges

## Slide 11: Thermal expansion problems
No room for thermal expansion
result  buckling

## Slide 12: Areas and volumes expand too!
cold
hot
cold
hot

## Slide 13: Does the whole get bigger or smaller when heated?
cold
hot
Both the inner and outer diameters
increase when the ring is heated

## Slide 14: Hot water causes the lid to expand, making it easier to unscrew it.

## Slide 15: Fire sprinklers are triggered by thermal expansion of a liquid

## Slide 16: Bi-Metal strips
thermal expansion of metals is put to good use in a bi-metallic strip.
it is two strips of different metals bonded together
metal A
metal B

## Slide 17: Heating a Bi-metal strip
when heat is applied to the bi-metallic strip, both metals expand, but by different amounts!
result:
The metal with the
higher thermal
expansion coefficient is on top
The red side expanded more
than the blue side, so the strip bends toward the blue side.

## Slide 18: Bi-Metal strip thermal switch used to turn power off when a preset temperature is reached
Used in coffee makers and hair dryers
ON
OFF

## Slide 19: Heat Flow
Heat is the energy that flows from one body to another because of their temperature difference
There are 3 ways that heat can be transferred:
  convection
  conduction
  radiation
HOT
COLD
HEAT

## Slide 20: Heat transfer by Convection
heat is transferred from one location to another by the bulk movement and subsequent mixing of liquids or gases (fluids), but NOT in solids.
when water is boiled, hot water at the bottom rises and mixes with cooler water at the top
Hot air rises:
  in winter, want hot air in at lower level
  in summer, cold air in at upper level
convection
currents
Notes: 20

## Slide 21: Heat transfer by conduction
heat is transferred directly through a material, with no bulk movement of material
only energy moves (molecules in a solid are not free to move, but can vibrate)
iron is a poor
conductor
of heat
Notes: 21

## Slide 22: heat conduction
HOT
COLD
Heat Flow
Cross sectional
area A
L
Heat Flow rate depends on A / L and a property
unique to the material, called thermal conductivity
Notes: 22

## Slide 23: Thermal Conductivity: a parameter that quantifies the ability of a material to conducting heat.
Material | Thermal conductivity
metals | 14 - 400
wood | 0.15
glass | 0.8
wool | 0.04
Goose down | 0.025
Styrofoam | 0.01
Metal | Thermal Conductivity
Silver | 406
Copper | 385
Aluminum | 205
Brass | 109
Iron | 80
Steel /SS | 50/14
Notes: 23

## Slide 24: Heat transfer by Radiation
The warmth you feel from the sun is the sun’s thermal radiation
It travels through the vacuum of space to reach earth, no material is necessary (takes 8 minutes)
you can feel its effects even though you cannot see the radiation.
you can feel the thermal radiation from a fireplace
Objects not in contact with liquids gases or other solids loose heat by radiation
Notes: 24

## Slide 25: Thermal Radiation
The amount of thermal radiation emitted by an object is proportional to its temperature raised to the fourth power ~ T4
Doubling the temperature will increase the amount of thermal radiation by 24 = 2 x 2 x 2 x 2 = 16
More on this next lecture